## Slide 1: Communication Protocols
Arti & Liz

## Slide 2: Communication Protocols
Bit transfer as a means of communication between different hardware devices
  High voltage indicates a 1 and low voltage indicates a 0
Considerations
  Serial vs. parallel
    One vs. multiple bits sent at a time
  Synchronicity
    Synchronized clocks between transmitting and receiving device
  Master-slave relationships
    Master device has control over slave devices
  Data Direction
    Half-duplex: both devices can communicate with each other but not simultaneously
    Full-duplex: both devices can communicate with each other simultaneously
Notes: Why not serial ports? (Asynchronous)
-Two systems with different clocks to communicate with each other
-Adds extra start and stop bits to help receiver sync at the start of each byte→ too much overhead
-Both sides must agree on the transmission speed

## Slide 3: Serial Peripheral Interface (SPI)
MOSI and MISO
  Master-out slave-in and master-in slave-out data lines
  Full-duplex
SCLK
  Clock line
  Synchronous
SS
  Slave select
  Supports one master multiple slaves

## Slide 4: Multiple-Slave Connections

## Slide 5: Inter-Integrated Circuit (I2C)
SDA
  Single data line
  Half-duplex
  Supports multiple masters multiple slaves
SCL
  Clock line
  Synchronous
Notes: Why not SPI?? (Requires more signal lines; undesirable when there are multiple slaves; Requires separate SS lines to each slave; Only allows one master)
Interview question: (multiple masters) before a master initiates a communication, how does it know if the line is busy?

## Slide 6: Code Along!

## Slide 7: 7 segment display counter using SPI
Arduino -------------- 7-Segment
5V -------------------- VCC
GND ------------------ GND
8 -------------------- SS
11 -------------------- SDI
13 -------------------- SCK

## Slide 8: 7 segment display counter using I2C
Arduino 7-Segment
5v ------------------------- VCC
GND --------------------- GND
SCL (A5: pin 19) ----- SCL
SDA (A4: pin 18) ----- SDA